SECTION 09 84 13

FIXED SOUND-ABSORPTIVE PANELS

– GENERAL

Specifier Note: Retain or delete paragraphs in Summary per project requirements.

SUMMARY

Section Includes:

Custom fabricated sound-absorptive wall panels.

Mounting accessories.

Related Sections:

Section 09 20 00 – Plaster and Gypsum Board

Section 09 70 00 – Wall Finishes

REFERENCES

ASTM C423 – Standard Test Method for Sound Absorption and Sound Absorption Coefficients by the Reverberation Room Method.

ASTM E84 – Standard Test Method for Surface Burning Characteristics of Building Materials

DEFINITONS

Noise Reduction Coefficient (NRC): Single number quantifier used to rate materials for their effectiveness in absorbing sound per ASTM C423.

SUBMITTALS

General: Provide listed submittals in accordance with Conditions of the Contract and Division 1 (Section 01 33 00) Submittal Procedures.

Product Data: Submit applicable reference standards, current performance data, application recommendations and product limitations.

Samples: Submit for approval two samples of the sound-absorptive panel not less than 12 inches by 12 inches.

Contract Closeout Submittals: (Refer to Section 01 78 00)

Operation (Section 01 78 23.13) and Maintenance Data (Section 01 78 23.16).

Warranty (Section 01 78 36) that all products shall perform in accordance with Contract Documents for a period of one (1) year from shipment and that any deficiencies shall be correctly promptly after receipt of written notice from Owner.

Specifier Note: Article below should include prerequisites, standards, limitations and criteria that establish an overall level of quality for products and workmanship for this section. Coordinate article below with Division 1 (Section 01 43 00) Quality Assurance.

QUALITY ASSURANCE

Installer's Qualifications: Installers shall have demonstrated experience in assembly and installation of products similar to those specified in this section.

Manufacturer's Qualifications: Manufacturer shall have demonstrated experience in fabrication of products similar to those specified in this section for a minimum of 5 years.

Fire Test Response Characteristics per ASTM-E84 Class A.

DELIVERY, STORAGE & HANDLING

General: Comply with Division 1 (Section 01 60 00) Product Requirements.

Delivery: Deliver materials in manufacturer’s original, unopened, undamaged containers with identification labels intact.

Storage and Protection: Store materials near installation point at temperature and humidity conditions recommended by the manufacturer.  Retain protective packaging.

FIELD CONDITIONS

Environmental Requirements: Do not install modules until all wet work is complete, the building is enclosed and temperature and humidity are similar to building conditions during occupancy.

- PRODUCTS

MANUFACTURERS

Basis of Design: AAPG InkSonics AP1

AAPG, 248 James Street, Venice, FL 34285; Telephone: (844) 307-9571; E-mail: pwest@aapgco.com. Web site: www.millworkusa.com

Substitutions: No Substitutions permitted

Performance Requirements

Minimum Sound Absorption Coefficients for Type A Mounting: NRC 0.75

Panel shall be of a 1” thick with sufficient rigidity to provide a panel flatness which shall not exceed a deflection of L/240 inches as measured diagonally across the panel.

Specifier Note: Select applicable panel model and base material.  Delete any options which are not relevant.

MATERIALS

Panel Construction:

AP1: 1” thick. Hemp Core. Wrapped edges.

AP2: 1-1/4” thick. Hemp Core. Wrapped edges.

AP3: ¾” Thick. Hemp Core. Wrapped edges.

Specifier Note: Select applicable panel model, thickness and color range.  Delete any options which are not relevant.

FABRICATION

Hemp Cores shall be framed to provide frontal and rear air chamber

Panels edges shall be wrapped and rear sealed.

Color/Image: Per manufacturers standard range

ACCESSORIES

All trim and closure trim shall be aluminum concealed fastening.

- EXECUTION

EXAMINATION

Verify that substrate conditions, which have been installed under other sections, are acceptable for product installation in accordance with manufacturer's instructions for installation.

Do not install panels until unsatisfactory conditions are corrected.

INSTALLATION

Comply with manufacturer's product data, installation instructions and product carton instructions for installation.

Install panels on room surfaces as indicated on the drawings.

CLEANING

Clean all surfaces according to manufacturer's recommendations.  Replace damaged components as directed by the Architect.

Remove all packaging and construction debris.

END OF SECTION